## Slide 1: ECE 447 Beyond Linear Control and Machine Learning
Spring 2019
Prof. Eric Klavins

## Slide 2: This Course
Linear
System
Linear Controller
Linear Estimator
+
-
r
y
u
x
^
K x
^
Plant is assumed linear (or linearized)
Plant is well understood
Goal is to track r
No randomness or substantial noise

## Slide 3: Next Courses
ECE 448: Control systems lab with hardware
ECE 449: Control systems capstone
Graduate courses
  547: Advanced linear control systems
  548: Linear multi-input / multi-output
  549: State estimation and system identification
  550: Optimal control (e.g. use the least energy)
  552: Power systems control
  570: Geometric control (e.g. robots, vehicles, manipulators)
  582: Digital control
  583: Nonlinear control
  585: Adaptive control (i.e. when the plant dynamics are drifting over time)
  593: Feedforward control
  594: Robust control (i.e. robust to disturbances, noise and uncertainty)
  597: Network control (e.g. control of swarms of robots)
Still linear
control systems

## Slide 4: Machine Learning
Often applied to classification problems
Tiger?
Puppy?
Fish?
…
Can be adapted to decision making and control
f𝜽(image) = species
Goal: find parameters 𝜽 to minimize number of misclassifications
Goal: find parameters 𝜽 to maximize expected reward
Reinforcement Learning

## Slide 5: Classification Examples
Takes labeled examples in.
Needs millions of images.
Once trained, is very good!
Image classification
Protein stability
Takes amino acid sequence
Predicts stability of the resulting protein
Trained on experimental data
Can use to predict stability of new proteins
https://www.ncbi.nlm.nih.gov/pubmed/28706065

## Slide 6: Examples of Reinforcement Learning
AlphaStar: Mastering the Real-Time Strategy Game StarCraft II

## Slide 7: Alpha Go: Deep Q-Learning
https://deepmind.com/blog/alphago-zero-learning-scratch/

## Slide 8: Physically realistic robot running

## Slide 9: Outline
Reinforcement learning
  http://rail.eecs.berkeley.edu/deeprlcourse-fa17/index.html#lectures
Neural networks
Q-learning (Reinforcement learning with neural networks)

## Slide 10: States, Actions and Rewards
Examples:
Video game: Action = move or fire, reward = score
Walking: Action = apply torque to joins, reward = distance traveled
Controls tasks: Action = input ut ,reward = 1 / error.
Chess: Action = move a piece, reward = 1 if action results in a win, 0 otherwise

## Slide 11: Policies
A policy is a parameterized probability distribution that says what to do in a given state, and is written
Parameter vector
State at step t
Action to take at step t
Probability of new state given
the old state and an action
Trajectories result from policies and the environment:

## Slide 12: Example: Goals and obstacles
States: (x,y) location
Rewards: -1, 0, or 10 depending on state
Action: up, down, right, left
Environment: Moves the requested direction unless at an edge
Policies: probability of going up, down, right, or left in each state.
=> A policy has 4 x width x height parameters (100 in this case)
Example trajectory: (0,0), up, (0,1), up, (0,2) up, (0,3), down, (0,2), right, (1,2), down, …

## Slide 13: Reinforcement Learning Goal
Find 𝜽 so that the expected sum of rewards over all trajectories is maximized.
J(𝜽)
Sum over sample trajectories produced by π𝜽.
Approximation: Just run policy π𝜽 a bunch of times to estimate the average reward.

## Slide 14: Maximizing J(𝜽) Using Gradient Assent
𝜽
J(𝜽)
Learning rate

## Slide 15: Approximating

## Slide 16: Approximating

## Slide 17: The REINFORCE Algorithm

## Slide 18: Example
Go to reinforce-map.ipynb
Questions:
  Given that trajectories are length 15, what is the maximum reward a trajectory could get?
  What happens when you increase the learning rate?
  What happens when you decrease the number of samples per epoch?
  Can you change the map to get it stuck in a local minima?

## Slide 19: Simple control example
x’ = 1.1 x + u
Discretize state
For each discretized state q, choose a u according to a normal distribution N(mq,vq)
The parameters are then mq,vq for q in the set of discretized states

## Slide 20: Limitations of REINFORCE
This term is called the “cost to go”.
Only a sample of a reward for a single trajectory.
What if we could come up with a model of the cost to go that was more accurate and remembered past trials?
r1
r2
r3
r4
r5

## Slide 21: Neural Networks